Frictional Force Lab

Purpose:  To determine the relationship between the force static friction and force normal,  kinetic friction and force normal, and surface area.

Apparatus and Procedure:  Friction Block (w/ selected surface), force sensor, assorted weights, computer, software

Procedure:

- Open Logger Pro, go to file “Probes and sensors”, choose force sensors, then choose dual range force, then click on 50 N Dual Range.mbl

- Mass the friction block and multiply the mass by 9.8 m/s2 to convert it to FN, then record in your data table under FN

- Hook empty force block to force sensor

- With slack (no force applied) on the sensor, zero the sensor

- Then hit collect, then slowly pull on the sensor so that it is parallel to the surface and moves at a constant rate once the block starts to move.

- Once the collection is completed, click on the examine button, then move the cursor to the first peak, record this value in your data table under Fs

- Then select the flat portion of the graph after the peak then click the statistics button to find the average force, record this value in your data table under Fk

- Add 200g (.2 kg) to the block and repeat steps 2-7 until you reach 12 trials

- Now repeat steps 3 – 8 with a different surface area.

- Once you have completed all twelve trials enter data to construct 4 graphs (Fs vs. FN and Fk vs. FN for each surface area)

- Analyze graphs to see if straightening is required and create mathematical model.

Data:

| Surface 1 | Surface 2 |
| --- | --- |
| FN (N) | Fs (N) | Fk (N) | FN (N) | Fs (N) | Fk (N) |

Evaluation of Data:

Mathematical Model ___________________  Mathematical Model ______________________

Mathematical Model ___________________  Mathematical Model ______________________

Conclusion:

# Text boxes

Force Sensor

Friction Block